ZIM.628.016.99

Wiper/Sunroof Voltage Converter

Installation in up thru 1961 356B T5 models

Congratulations on your purchase of our high quality voltage reducing converter for use in your vehicle. It has been designed & assembled for ease of installation and years of quality service.

Warning !  This unit is preset for a steady 6 volt supply and no more load than 15 amps. Any testing or checking out its circuits is unnecessary & will damage the unit. Wire it properly as instructed & it will work just as designed. All units are tested before shipping. Never exceed a load of 15 amps with this device or damage to the unit will occur & NO warranty will be issued. Connect all wires as indicated. This unit is for negative ground systems only. The RED wire is connected to the 12 volt power source. The YELLOW wire is connected to the old 6 volt supply wire to the wiper motor. The BLACK wire MUST be connected to a known good chassis ground or damage will occur. Make sure where you ground the terminal the area is clean of any debris or paint so as to make a solid good ground.

Find a good mounting position that will allow max air flow around the device. The voltage reduction process creates heat. This heat must be allowed to dissipate into the air. DO NOT stuff it behind any carpeting or insulation where there is no airflow. It is normal for the unit to get hot to the touch. The large fins on the heat sink dissipate this heat.

On the up to T5 cars, we suggest you remove the passenger side toe board, & mount the unit down in the foot well behind the carpet & toe board. BE CAREFUL THE GAS TANK IS LOCATED DIRECLTY IN FRONT OF THIS FIREWALL BUT UP HIGHER!!! Just be aware of where it is & DO NOT drill into it. You can either mount it to the forward wall facing the front of the car on the vertical surface of the firewall, or you can move it over the right & mount it to the vertical wall which is the back side of the passenger side inner fender well. Drill small holes & use the included hardware to mount the device to the sheet metal panel of your choice. The black wire from the unit MUST be grounded. Make sure it makes good ground contact by scraping away any paint to insure metal to metal contact & crimp an eyelet connector on the black wire. This black wire MUST be grounded for the unit to work properly. Damage to the unit will occur if this is not done.

Run the RED and YELLOW wires up into the back of the metal tubing conduit that routes the wires up to the fuse box. You might have to take a small piece of stiff wire to stick down from the top by the fuse box to the bottom & attach the wires to it to pull it back up though the conduit.

Locate the fuse panel under the dash on the passenger side (inside the car) of the vehicle & remove the cover. The bottom (foreword position) of the fourth fuse from the right has two (2) BLACK wires with PURPLE tracers. This fuse operates the wipers & interior lights. CAREFULLY, with a small screwdriver disconnect one of these wires. Turn on the key & check the wipers. If they DO NOT operate, you have the correct wire. If the wipers still work, replace that wire & choose the other wire and remove it from the fuse connector. Now try the wipers again and they should NOT work.  Attach this wiper supply wire with a crimp connector to the YELLOW wire marked 6 volts of the converter unit. You can shorten the YELLOW wire if you desire as there is much more wire than needed. Place the end of the RED wire from the convertor marked 12 volts back into the fuse position you removed the original wire to the wipers from. Gently tighten the screw to secure the wire. Bundle any wires hanging down neatly using supplied zip ties. Replace  toe board and carpeting.        SEE NEXT PAGE FOR T6 CARS

ZIM.628.016.99

Wiper/Sunroof Voltage Converter

Installation in 1962 on 356B &C, T6 models

Congratulations on your purchase of our high quality voltage reducing converter for use in you vehicle. It has been designed and assembled for ease of installation and years of quality service.

Warning !  This unit is preset for a steady 6 volt supply and no more load than 15 amps. Any testing or checking out its circuits is unnecessary & will damage the unit. Wire it properly as instructed & it will work just as designed. All units are tested before shipping. Never exceed a load of 15 amps with this device or damage to the unit will occur & NO warranty will be issued. Connect all wires as indicated. This unit is for negative ground systems only. The RED wire is connected to the 12 volt power source. The YELLOW wire is connected to the old 6 volt supply wire to the wiper motor. The BLACK wire MUST be connected to a known good chassis ground or damage will occur. Make sure where you ground the terminal the area is clean of any debris or paint so as to make a solid good ground.

Find a good mounting position that will allow max air flow around the device. The voltage reduction process creates heat. This heat must be allowed to dissipate into the air. DO NOT stuff it behind any carpeting or insulation where there is no airflow. It is normal for the unit to get hot to the touch. The large fins on the heat sink dissipate this heat.

On T6 cars that you remove the plastic trunk liner mat & mount the unit in the front trunk area on the drivers side near the back of the trunk compartment just under the fresh air box Zip tie the unit to the front trunk cable release tube. If you wish you can mount it elsewhere using the supplied hardware, but the above mentioned place is the easiest & quickest & is close to the fuse box.

The black wire from the unit marked ground must be grounded for the unit to work properly. Damage to the unit will occur if this is not done. Find a good place to attach this wire to a good clean ground. Use an eyelet terminal crimped on the end of the wire to connect. You may use some of the hardware supplied to drill a hole into the fender well & attach the black wire to. Scrape away any paint to bare metal.

Locate the fuse box on the same side of the inner trunk forward of where you have mounted the convertor unit. Remove the fuse box cover. Run the YELLOW & RED wires up to the fuse box. Locate the bottom (foreword position) of the fourth fuse from the right. The two (2) BLACK wires with PURPLE tracers. This fuse operates the wipers & interior lights. CAREFULLY, with a small screwdriver disconnect one of these wires. Turn the key on & check the wipers. If they DO NOT operate, you have chosen the correct wire. If the wipers still work, put that wire back & choose the other wire & remove it from the fuse connector. Now try the wipers again & they should NOT work.  Attach this wiper supply wire with a crimp connector to the YELLOW wire marked 6 volts of the converter unit. You can shorten the YELLOW wire if you desire. Place the end of the RED wire from the convertor marked 12 volts back into the fuse position you removed the original wire to the wipers. Shorten this wire if needed. Gently tighten the screw to secure the wire. Bundle up any of the wires using the supplied zip ties. Re-install the plastic trunk liner mat & Replace cover back on the fuse box.

SEE NEXT PAGE FOR UP TO T5 CARS

EACH and EVERY one of these units is bench tested for several minutes

BEFORE being boxed by us. This is to ensure proper operation of every unit

Test input voltage _____________

Output voltage ______________

Operating temperature ____________ f

Tested by ____________